# TRAFFIC SIGNAL GENERAL NOTES

- ALL WORK SHALL CONFORM TO THE 2014 CALIFORNIA MANUAL ON UNIFORM TRAFFIC CONTROL DEVICES (CA MUTCD), THE STATE OF CALIFORNIA DEPARTMENT OF TRANSPORTATION (CALTRANS) STANDARDS PLANS AND SPECIFICATIONS (2015 EDITION), AND SPECIAL PROVISIONS, AND ALL ADDENDUM THERETO.

- ALL SIGNS SHALL BE STANDARD SIZE UNLESS OTHERWISE NOTED ON PLANS.  SIGN LOCATION SHALL BE VERIFIED IN THE FIELD BY THE ENGINEER.

- ALL STRIPES, SIGNS, AND PAVEMENT MARKINGS SHALL BE REFLECTORIZED.  STENCILS FOR PAVEMENT MARKINGS SHALL MATCH CITY STANDARD STENCILS EXACTLY.  ALL STRIPING, MARKING DETAILS, AND RAISED PAVEMENT MARKERS SHALL MATCH CALTRANS STANDARD PLANS DETAILS AND SPECIFICATIONS.

- PAINTED TRAFFIC STRIPES AND PAINTED PAVEMENT MARKINGS (IF ALLOWED) SHALL BE APPLIED IN TWO COATS.  PAVEMENT MARKINGS SHALL BE APPLIED IN THERMOPLASTIC FORMAT, UNLESS APPROVED OTHERWISE.

- ALL EXISTING SIGNS TO REMAIN SHALL BE PROTECTED IN PLACE, UNLESS OTHERWISE NOTED.

- CONFLICTING SIGNS AND RAISED PAVEMENT MARKERS SHALL BE REMOVED.  ALL REMOVAL OF SIGNS AND MARKINGS SHALL BE THE RESPONSIBILITY OF THE CONTRACTOR.

- ALL CONFLICTING STRIPING AND PAVEMENT MARKING SHALL BE REMOVED BY SANDBLASTING OR GRINDING AS DIRECTED BY THE ENGINEER, UNLESS OTHERWISE NOTED.

- NEW CONDUCTOR CABLES SHALL BE USED FOR TRAFFIC SIGNAL, AND STRANDED WIRES FOR SAFETY LIGHTS AND INTERNALLY ILLUMINATED STREET NAMES SIGNS (IISNS).

- PEDESTRIAN PUSH BUTTON SHALL CONFIRM TO ADA REQUIREMENTS. PEDESTRIAN INDICATIONS SHALL BE LED PEDESTRIAN/HAND TYPE. TRAFFIC SIGNAL INDICATIONS SHALL BE 12” LENSES WITH METAL BACKPLATES AND VISORS, ETC. ALL INDICATIONS SHALL BE “LED” TYPE. IISNS SHALL BE RETROFITTED LED PER SPEC.

- PRIOR TO BORING, JACKING OR TRENCHING OF ANY CONDUIT, THE CONTRACTOR SHALL CONTACT ALL UTILITY COMPANIES FOR EXACT LOCATION OF UTILITIES. NOTE: “TRENCHING IN PAVEMENT METHOD” IS NOT AN OPTION.  ALL POT HOLES SHALL BE HAND DUG.  SAW CUTTING POT HOLE LOCATIONS IS NOT AN OPTION.

- THE CITY WILL PAY THE EDISON COMPANY, ALL APPROPRIATE SERVICE INSTALLATION CHARGES. THE CONTRACTOR SHALL MAKE ARRANGEMENTS WITH THE EDISON COMPANY FOR SERVICE CONNECTIONS. AT LEAST 48 HOURS ADVANCE NOTICE SHALL BE GIVEN TO THE EDISON COMPANY BY CONTACTING THEIR ENGINEER AT 909-592-3725.

- ALL MATERIAL AND WORK SHALL CONFORM TO THE CURRENT CITY STANDARD PLANS AND THE STANDARD PLANS AND SPECIFICATIONS OF THE CALIFORNIA DEPARTMENT OF TRANSPORTATION.  ALL ELECTRICAL WORK SHALL BE DONE IN ACCORDANCE WITH THE LATEST EDITION OF CALTRANS STANDARD SPECIFICATIONS, SECTION 86.  IF THERE IS A CONFLICT BETWEEN CALTRANS AND CITY SPECIFICATIONS, THE CITY SPECIFICATIONS WILL PREVAIL.

- FINAL FIELD LOCATIONS OF ALL EQUIPMENT SHALL BE APPROVED BY THE CITY INSPECTOR PRIOR TO INSTALLATION.

- PULL BOXES SHALL BE NO. 6E, EXCEPT AS SHOWN.  PULL BOXES SHALL BE CRISTY N36 ELECTRICAL BOX WITH FIBRELYTE LID WITH N90 BOLT DOWN KIT.

- MINOR ERRORS OR OMISSIONS ON THESE PLANS OR IN THE ACCOMPANYING SPECIFICATIONS SHALL NOT RELIEVE THE CONTRACTOR FROM PROVIDING A COMPLETE AND FULLY OPERATING SYSTEM.

- EXISTING STREET LIGHTS TO BE REMOVED SHALL BE SALVAGED TO THE CITY YARD.  CONTACT TRAFFIC OPERATIONS CREW CHIEF AT (909) 620-2395, 48 HOURS PRIOR TO DELIVERY.

- SIGNS AND POSTS TO BE REMOVED SHALL BE SALVAGED TO CITY YARD.  CONTACT PAINT AND SIGN SHOP AT (909) 620-2397, 48 HOURS PRIOR TO DELIVERY.

- ALL EXISTING STRIPING AND PAVEMENT MARKINGS SHALL BE REPLACED ON ALL APPROACHES WITHIN 300 FEET OF THE INTERSECTION. ALL STRIPING, MARKING DETAILS, AND RAISED PAVEMENT MARKERS SHALL MATCH CITY STANDARD PLANS, DETAILS, AND SPECIFICATIONS. ALL STRIPING AND PAVEMENT MARKINGS SHALL BE IN THERMOPLASTIC UNLESS OTHERWISE NOTED.

- GROUT THE BOTTOM OF ALL PULL BOXES, MINIMUM OF 2” THICK. SLOPE THE GROUT TO A 1 ½” DIAMETER DRAIN HOLE IN THE GROUT TO ALLOW WATER TO DRAIN THROUGH THE GROUT TO THE UNDERLYING CRUSHED ROCK.

- PAINT ALL POLES, CABINETS, TRAFFIC SIGNAL EQUIPMENT, AND MOUNTINGS (VISIBLE TO THE PUBLIC) WITH SAN DIMAS BROWN. THE ONLY BLACK IS THE TRAFFIC SIDE OF BACK PLATE, INSIDE THE VISORS, AND THE PED CRATE (IN PEDESTRIAN INDICATION).  *******CHECK WITH CITY BEFORE INCLUDING THIS NOTE**********